## Slide 1: Assignments and Arithmetic Operators
ELEC1006: ENGINEERING COMPUTING

## Slide 2: Operators
PAGE 2
Assignment (=)
Arithmetic operators (+, -, *, /, %)
Compound assignment (+=,-=,*=,/=, %=, >>=,<<=, &=, ^=, |=)
Increase and decrease (++, --)
Relational and equality operators (<, >, <=, >=, ==, !=)
Logical operators (!, &&, ||)
Bitwise operators (&, |, ^, ~, <<, >>)
Conditional operator (?)
Comma operator (,)
Bitwise operator
Explicit type casting operator
Precedence of operators

## Slide 3: Assignment (=)
PAGE 3
Assignment operator assigns a value to a variable
  a=5;
Most important rule in ‘assignment’ is ‘right-to-left’, i.e., the operation always takes place from the right to left. a=b; (whatever in a will be overwritten by the contents of b)
a=2+(b=5); b=5; a=2+b;
a=b=c=5; c=5; b=c; a=b;

## Slide 4: Multiple Assignments
PAGE 4
The = can be used to assign a value to multiple variables:
  x = y = z = 5;
Value of = is the value that is assigned
Associates right to left:
  x = (y = (z = 5));

## Slide 5: Combined Assignment
PAGE 5
Look at the following statement:
  sum = sum + 1;
  sum + 1 adds 1 to the variable sum and stores the result back into variable sum using the assignment =.
Old value
of sum
New value
of sum

## Slide 6: Assignments & Arithmetic Operators
PAGE 6
Statement | What It Does | Value of X after the statement
X = X + 4; | Adds 4 to X | 10
X = X – 3; | Subtracts 3 from X | 3
X = X * 10; | Multiplies by 10 | 60
X = X / 2; | Divides X by 2 | 3
X = X % 4; | Makes X the remainder of X/4 | 2
X = 6;

## Slide 7: Arithmetic Operators (+, - , *, /, %)
% is the modulo operation (not a percentage calculation) – it calculates the remainder of the division between the two values:
Algebraic Expressions
PAGE 7
Algebraic Expression | Operation | C++ Equivalent
2x | 2 times x | 2 * x
(4)(7) | 4 times 7 | 4 * 7
3ab | 3 times a times b | 3 * a * b

## Slide 8: Algebraic Expressions
PAGE 8
Multiplication requires an operator:
  Area=lw is written as Area = l * w;
There is no exponentiation operator:
  Area=s2 is written as Area = pow(s, 2);
Parentheses may be needed to maintain order of operations:
  is written as
  m = (y2-y1) /(x2-x1);
  NOT
  m = y2-y1/x2-x1;

## Slide 9: Compound Assignment
PAGE 9
a += 5; a = a + 5;
a -= 5; a = a - 5;
a /= b; a = a / b;
a *= b+1; a = a * (b+1);
Increase and decrease
a += 1;
a ++;
a = a + 1;

## Slide 10: Compound Assignment
PAGE 10
Increase and decrease
a += 1;
a ++;
a = a + 1;
++a ;
a = a + 1;
c=a*b;
a=a++;
c=a ++*b;
a=a++;
c=a*b;
c=++a *b;
If a=2, b=5
c=10;
a=3;
a=3;
c=15;
Same rules apply to --

## Slide 11: More info on C++
PAGE 11
[1] cplusplus.com: Operators
https://cplusplus.com/doc/tutorial/operators/

## Slide 12: Other Common Operators
ELEC1006: ENGINEERING COMPUTING

## Slide 13: Operators
PAGE 13
Assignment (=)
Arithmetic operators (+, -, *, /, %)
Compound assignment (+=,-=,*=,/=, %=, >>=,<<=, &=, ^=, |=)
Increase and decrease (++, --)
Relational and equality operators (<, >, <=, >=, ==, !=)
Logical operators (!, &&, ||)
Bitwise operators (&, |, ^, ~, <<, >>)
Conditional operator (?)
Comma operator (,)
Bitwise operator
Explicit type casting operator
Precedence of operators.

## Slide 14: Relational and Equality Operators
PAGE 14
e.g. a=2, b=3, c=6;
Used to evaluate a comparison between two expressions
== is not the same as =
What will this statement produce b=2==a ?????

## Slide 15: Logical Operators
PAGE 15
! Is the logic NOT operation (only has ONE operand)
&& is the logic AND operation (needs TWO operand)
|| is the logic OR operation (Two operand)
e.g. a=3, b=5;
!(a==b) is true (similar to a!=b)
(a>3)&&(b<7) is false
(a>3)||(b<7) is true

## Slide 16: Conditional Operator
PAGE 16
Evaluates an expression returning a value if that expression is true and a different one if the expression is false.
Its format is:
condition ? result1 : result2
True – result 1
False – result 2

## Slide 17: Comma Operator
PAGE 17
Used to separate two or more expressions that are included where only one expression is expected
When the set of expressions has to be evaluated for a value, only the rightmost expression is considered:
a = (b = 2, b+3); b=2; a=b+3;

## Slide 18: Bitwise Operator (***)
PAGE 18
Input 1 | Input 2 | AND | OR | XOR
0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 1 | 1
1 | 0 | 0 | 1 | 1
1 | 1 | 1 | 1 | 0
Truth Table
Single bit operations.
1 bit only has binary (2) states.
  0 (FALSE) or 1 (TRUE).
NOT inverts states, i.e. 1 → 0 and 0 → 1.
Refer to the Truth Table for the possible states.
SHL refers to shift left operation:
  001 → 010.
SHR refers to shift right operation:
  110 → 011.

## Slide 19: Type Casting Operator
PAGE 19
Operations are performed between operands of the same type.
If not of the same type, C++ will convert one to be the type of the other
This can impact the results of calculations.
e.g.: float a=10.0;
int b=4;
int c=a/b;
c = 2 instead of c = 2.5 due to c
being an integer instead of float.

## Slide 20: Precedence of Operators
PAGE 20

## Slide 21
Precedence | Operator | Description | Associativity
1 | :: | Scope resolution | Left-to-right →
2 | a++ a-- | Suffix/postfix increment and decrement | 
 | type() type{} | Functional cast | 
 | a() | Function call | 
 | a[] | Subscript | 
 | . -> | Member access | 
3 | ++a --a | Prefix increment and decrement | Right-to-left ←
 | +a -a | Unary plus and minus | 
 | ! ~ | Logical NOT and bitwise NOT | 
 | (type) | C-style cast | 
5 | a*b a/b a%b | Multiplication, division, and remainder | 
6 | a+b a-b | Addition and subtraction | 
 |  |  | Left-to-right →
7 | << >> | Bitwise left shift and right shift | 
8 | <=> | Three-way comparison operator (since C++20) | 
 |  |  | Left-to-right →
9 | < <= > >= | For relational operators < and ≤ and > and ≥ respectively | 
 |  |  | Left-to-right →
10 | == != | For equality operators = and ≠ respectively | 
11-13 | &, ^, ¦ | Bitwise AND, XOR and OR | 
 |  |  | Left-to-right →
14 | && | Logical AND | 
15 | ¦¦ | Logical OR | 
16 | a?b:c | Ternary conditional[note 2] | Right-to-left ←
 | = | Direct assignment (provided by default for C++ classes) | 
 | += -= | Compound assignment by sum and difference | 
 | *= /= %= | Compound assignment by product, quotient, and remainder | 
 | <<= >>= | Compound assignment by bitwise left shift and right shift | 
 | &= ^= ¦= | Compound assignment by bitwise AND, XOR, and OR | 
17 | , | Comma | Left-to-right →

## Slide 22: More info on C++
PAGE 22
[1] cplusplus.com: Operators
https://cplusplus.com/doc/tutorial/operators/

## Slide 23: if Conditional Branch
ELEC1006: ENGINEERING COMPUTING

## Slide 24: Conditional Branches
PAGE 24
Defined as a condition that causes the program to change the path of execution based on the value of an expression.
Forms of conditional branches:
  if statement. ←
  switch statement.

## Slide 25: if Statement
PAGE 25
The ‘if’ (a keyword) is to execute a statement or a block of statements only if a condition is satisfied. The form is:
  if (condition) statement
  e.g. if (x>90)
      cout << “A very good score!” << endl;
  This ‘cout statement’ will only be executed if the value in x is greater than 90.

## Slide 26: Multiple Lines of Code
PAGE 26
  if multiple lines of code is to be executed under an if statement, {} should be used.
  Do NOT put ; after the if (condition) statement.
  e.g. if (x>90)
      {
      cout << “Congratulation!”<< endl;
      cout << “A very good score of ”;
      cout << x << “.” << endl;
      }

## Slide 27: Two Conditional Branches
PAGE 27
  The else statement can be used to specify what to do if the ‘if’ condition is not met.
  e.g. if (x>90) // Condition 1
      cout << “Congratulation!”<<endl;
      else // Condition 2
      cout << “You can improve your score”;

## Slide 28: Multiple Conditional Branches
PAGE 28
  Use if – else if – else for a range of conditional branches.
  e.g.
    if (x<0) // Condition 1
      cout << “x is negative.”<<endl;
      else if (x>0) // Condition 2
      cout << “x is positive.”<<endl;
      else // Condition 3
      cout << “x is 0.” <<endl;

## Slide 29: Commas in if Statement
PAGE 29
  Use of commas ,
  e.g.
  int a=1,b=2,c=10,d=20;
  if (a<0) c*=10, d*=20;
  else if (a<b) c/=10, d/=20;
  else c=b;

## Slide 30: Previous code is equivalent to:
PAGE 30
  int a=1;
  int b=2;
  int c=10;
  int d=20;
  if (a<0)
  {
  c=c*10;
  d=d*20;
  }
  else if (a<b)
  {
  c=c/10; d=d/20;
  }
  else
  c=b;
  Too long? – But, use this!

## Slide 31: More info
PAGE 31
[1] cplusplus.com: Statements and flow control
https://cplusplus.com/doc/tutorial/control/
[2] learncpp.com: 5.2 – If statements
https://www.learncpp.com/cpp-tutorial/52-if- statements/

## Slide 32: switch Conditional Branch
ELEC1006: ENGINEERING COMPUTING

## Slide 33: Conditional Branches
PAGE 33
Defined as a condition that causes the program to change the path of execution based on the value of an expression.
Forms of conditional branches:
  if statement.
  switch statement. ←

## Slide 34: switch Statement
PAGE 34
switch statement is a natural choice for menu-driven program:
  display the menu
  then, get the user's menu selection
  use user input as expression in switch statement
  use menu choices as expr in case statements
if-else can be used in place of switch.

## Slide 35: switch Statement Format
PAGE 35
switch (expression) //integer
{
case exp1: statement1;
case exp2: statement2;
...
case expn: statementn;
default: statementn+1;
}

## Slide 36: break Statement
PAGE 36
Used to exit a switch statement
If it is left out, the program "falls through" the remaining statements in the switch statement
Example:
switch (n) {
case ’a':
cout << ”a has been given.\n";
break;
case ’b':
cout << ”b has been given.\n";
break;
default:
cout << "unknown character!\n";
break;
}

## Slide 37: Alternative Program
PAGE 37
Use if - else if - else statement as an alternative to switch:
Example:
if (n == ‘a’)
cout << ”a has been given.\n";
else if (n == ’b’)
cout << ”b has been given.\n";
else
cout << "unknown character!\n";
}

## Slide 38: More info
PAGE 38
[1] cplusplus.com: Statements and flow control
https://cplusplus.com/doc/tutorial/control/
[2] learncpp.com: 5.3 – Switch statements
https://www.learncpp.com/cpp-tutorial/53-switch- statements/
[3] cppreference.com: switch statement https://en.cppreference.com/w/cpp/language/switch

## Slide 39: while Iteration Statement
ELEC1006: ENGINEERING COMPUTING

## Slide 40: Iteration Statement (loops)
PAGE 40
Loops are used to repeat a statement a certain number of times when a condition is met.
There are three types of loops:
  while loop. ←
  do-while loop.
  for loop.

## Slide 41: The while Loop
PAGE 41
The format is:
  while (expression or condition) { Statement(s) }
  – repeat while “expression or condition” is true.
  The logical flow of while loop:

## Slide 42: Example
PAGE 42
// custom countdown using while
#include <iostream>
using namespace std;
int main ()
{
int n;
cout << "Enter the starting number: ";
cin >> n;
while (n>0) // Don’t put ; at the end
{
cout << n << ", ";
--n; // Decrement n by 1 in every loop
}
cout << "FIRE!\n";
return 0;
}

## Slide 43: Input validation
PAGE 43
cout << "Enter a number less than 10: ";
cin >> number;
while (number >= 10)
{
cout << "Invalid Entry!" << "Enter a number less than 10: ";
cin >> number;
}

## Slide 44: Tips: When to use while
PAGE 44
Use while statement when the number of times the loop is required to run is unknown.
Use while (1) to form an infinite loop especially when using a simple program that runs for long periods of time, e.g. mobile phone call:
while (1)
{
read_input(); // 1) Get network data
process_data(); // 2) Convert into sound signal
output_data(); // 3) Play signal on speaker
if call_end()
break; // Break the while loop if call ends
}

## Slide 45: More info
PAGE 45
[1] cplusplus.com: Statements and flow control
https://cplusplus.com/doc/tutorial/control/
[2] learncpp.com: 5.5 – While statements
https://www.learncpp.com/cpp-tutorial/55-while- statements/

## Slide 46: do-while Iteration Statement
ELEC1006: ENGINEERING COMPUTING

## Slide 47: Iteration Statement (loops)
PAGE 47
Loops are used to repeat a statement a certain number of times when a condition is met.
There are three types of loops:
  while loop.
  do-while loop. ←
  for loop.

## Slide 48: The do-while Loop
PAGE 48
The format is:
  do { statements } while (expression or condition);
  Only difference with the while statement is that do-while evaluates the condition after executing the statements.
while Loop Logic
do-while Loop Logic

## Slide 49: Example
PAGE 49
// Number echo
#include <iostream>
using namespace std;
int main ()
{
unsigned long n;
do {
cout << "Enter number (0 to end): ";
cin >> n;
cout << "You entered: " << n << "\n";
} while (n != 0); // Must use ;
return 0;
}

## Slide 50: Notes on do-while
PAGE 50
Loop always executes at least once.
Execution continues as long as the expression is true and stops the repetition when the expression becomes false.
Useful in menu-driven programs to bring user back to menu to make another choice.

## Slide 51: Menu –driven Program
PAGE 51
#include <iostream>
using namespace std;
int main()
{
int selection; // Selection variable
do {
cout << "Please make a selection: \n"; // List menu
cout << "1) Addition\n";
cout << "2) Subtraction\n";
cout << "3) Multiplication\n";
cout << "4) Division\n";
cin >> selection; // Get user menu selection
} while (selection != 1 && selection != 2 && selection != 3 && selection != 4);
// Do something with the selection here
return 0;
}

## Slide 52: More info
PAGE 52
[1] cplusplus.com: Statements and flow control
https://cplusplus.com/doc/tutorial/control/
[2] learncpp.com: 5.6 – Do while statements
https://www.learncpp.com/cpp-tutorial/56-do-while- statements/

## Slide 53: for Iteration Statement
ELEC1006: ENGINEERING COMPUTING

## Slide 54: Iteration Statement (loops)
PAGE 54
Loops are used to repeat a statement a certain number of times when a condition is met.
There are three types of loops:
  while loop.
  do-while loop.
  for loop. ←

## Slide 55: The for Loop
PAGE 55
for loop is used when we know how many iterations (loops) are required.
Test each expression before each iteration in the for loop and so, it is known as a pre-test loop similar to while loop.
  Note: do-while loop is known as a post-test loop, where the statements executed at least once (one iteration) before the expression is checked.

## Slide 56: for Loop Syntax
PAGE 56
The format is:
  for (initialisation; expression; increase or decrease)
  {
  statements
  }
  – Note: No ; after the )
  The mechanics:
  Perform initialisation
  Evaluate test expression
    If true, execute statement
    If false, terminate loop execution
  Execute update, then re-evaluate test expression
Test
Update

## Slide 57: Example
PAGE 57
Flowchart
for (int count = 1; count <= 5; count++)
{
cout << "Hello" << endl;
}

## Slide 58: while Loop Equivalent
PAGE 58
for (int count = 1; count <= 5; count++)
{
  cout << "Hello" << endl;
  }
for loop is like an advanced while loop
int count=1;
while (count <= 5)
{
cout << "Hello" << endl;
count++;
}

## Slide 59: Variations using commas
PAGE 59
Can also have multiple initialisation and update expressions. Separate the statements with commas ,: int x, y; for (x=1, y=1; x <= 5; x++, y++) { cout << x << " plus " << y << " equals " << (x+y) << endl; }
Initialisations
updates

## Slide 60: Scope of Variables
PAGE 60
You can declare variables in the initialisation expression.
Variable i only exist in the for loop { … }, not outside of it.
  int sum = 0;
  for (int i = 0; i <= 10; i++)
  {
  sum += i; // sum = sum + i
  }

## Slide 61: More info
PAGE 61
[1] cplusplus.com: Statements and flow control
https://cplusplus.com/doc/tutorial/control/
[2] learncpp.com: 5.7 – For statements
https://www.learncpp.com/cpp-tutorial/57-for- statements/

## Slide 62: Nested Loops & Exit Statement
ELEC1006: ENGINEERING COMPUTING

## Slide 63: Combining Loops
PAGE 63
Loops can be combined together (nested loops).
  The statement within a loop can contain another loop:
int i, j;
for (i = 0; i < 4; i++)
{
for (j = 0; j < 4; j++)
{
// statements
}
}

## Slide 64: Nested Loops
PAGE 64
Inner loop goes through all repetitions for each repetition of outer loop
Inner loop repetitions complete sooner than outer loop
Total number of repetitions for inner loop is the product of number of repetitions of the two loops.

## Slide 65: exit() Statement
PAGE 65
Use exit(n) to exit the program.
  n is a specific exit code:
    0 for successful exit.
    1 or non-zero number for failure as mentioned below.

## Slide 66: Example
PAGE 66
#include <iostream>
using namespace std;
int main ()
{
unsigned long n=1;
for (n; n<5; n++)
{
cout << "hello world\n";
if(n==2)
exit(1);
}
cout << "this is the end of the program.";
return 0;
}

## Slide 67: More info
PAGE 67
[1] cplusplus.com: Statements and flow control
https://cplusplus.com/doc/tutorial/control/
[2] cplusplus.com: function exit
https://cplusplus.com/reference/cstdlib/exit/?kw=exit
[3] learncpp.com: 5.7 – For statements
https://www.learncpp.com/cpp-tutorial/57-for- statements/
[4] Exit codes in C/C++ with Examples
https://www.geeksforgeeks.org/exit-codes-in-c-c-with- examples/